Alfvén Stats 5—Thresholds and Screenings
CONTENTS
1. Thresholds in Alfvén_Stats_5
2. Where thresholds are applied
3. How mapping to ionosphere takes place
4. Which quantities get mapped
  1. Quantities integrated over entire interval that get mapped
5. How quantities attributable to AWs are distinguished from others
### Thresholds in Alfvén_Stats_5
current_threshold=1.0 ;microA/m^2
delta_b_threshold=5.0 ; nT
delta_E_threshold=10.0 ; mV/m
esa_j_delta_bj_ratio_threshold=0.02
electron_eflux_ionos_threshold=0.05 ;ergs/cm^2/s
eb_to_alfven_speed=10.0
→factor by which the event can differ from model Alf speed and still be called an Alfven wave
→(applies only to the lower limit for e over b the upper limit is taken care of by the requirement that delta_b exceed 5 nT)
energy_electrons=[0.,30000.] ;use 0.0 for lower bound since the sc_pot is used to set this
energy_ions=[0.,500.] ;use 0.0 for lower bound since the sc_pot is used to set this
### Where thresholds are applied
current_threshold=1.0 ;microA/m^2
→Applied L797
→Note, jtemp is unsigned:
deltaBX=deriv(position,magz.y)
jtemp=abs(1.0e-3*(deltaBx)/1.26e-6) ;(L677)
→Code:
        jmax=max(jtemp(intervalfields),indjmax)
        current_intervals(j,4)=jmax*sign_jtemp(start_points(j))
        if jmax LE current_threshold then begin
        current_intervals(j,3)=0.0
        endif

delta_b_threshold=5.0 ; nT
→Applied L956
→ Calculation of db (L952):
db=max(magz.y(intervalfields))-min(magz.y(intervalfields))
        median_db=median(magz.y(intervalfields))
→Code:
if db LT delta_b_threshold then current_intervals(j,3)=0.0

delta_E_threshold=10.0 ; mV/m
→Applied L967
→ Calculation of de (L963):
        de=max(efield_smooth)-min(efield_smooth)
        median_de=median(fields.comp2(intervalfields))
→Note, efield_smooth is elec field amplitude smoothed to below proton gyro freq.
→Code:
        current_intervals(j,18)=de
        current_intervals(j,25)=median_de
        if de LT delta_E_threshold then current_intervals(j,3)=0.0

esa_j_delta_bj_ratio_threshold=0.02
→Applied L810
→Code (L805-12)
        ;;get the electron current and determine if to keep this event
        sign=-1.*je_tmp_data(intervalparts_electrons)/abs(je_tmp_data(intervalparts_electrons))
        maxJe=max(abs(je_tmp_data(intervalparts_electrons)),ind)
        maxJe=maxJe*sign(ind)*1.6e-9 ;;in microA/m2
        current_intervals(j,5)=maxJe
        if abs(maxJe)/abs(jmax) LE esa_j_delta_bj_ratio_threshold then begin
        current_intervals(j,3)=0.0
        endif

electron_eflux_ionos_threshold=0.05 ;ergs/cm^2/s
→Note that this considers flux integrated over all angles, not just downgoing electrons
→Note that the screening is that both maxJEe_ionos be less than e_eflux_ionos_threshold AND that [max(e- flux integrated over all angles) – max(down e- flux)] be less than e_eflux_ionos_threshold
→Applied L833
→ See calculation of jee_ionos under 'Which quantities get mapped'
→Code (L831-5)
        current_intervals(j,6)=maxJEe_ionos
        current_intervals(j,40)=maxJEe_tot_ionos
        if abs(maxJEe_ionos) LE electron_eflux_ionos_threshold and abs(maxJEe_tot_ionos-maxJEe_ionos) LE electron_eflux_ionos_threshold then begin
        current_intervals(j,3)=0.0
        endif

eb_to_alfven_speed=10.0
→ “factor by which … can differ from model Alfven speed and still be called an Alfven wave”
→NOTE “(applies only to the lower limit for e over b the upper limit is taken care of by the requirement that delta_b exceed 5 nT)”
→Note that VA is calculated by feeding alfven_speed_mlt altitude [21] and MLT [22]
→Applied L1008
→Code (L1005-8)
        ;;e over b test
        va=1000.0*alfven_speed_mlt(current_intervals(j,21),current_intervals(j,22))
        e_over_b=(1.0e-3*current_intervals(j,18))/(current_intervals(j,17)*1.0e-9)
        if e_over_b/va LT 1.0/eb_to_alfven_speed then current_intervals(j,3)=0.0

energy_electrons=[0.,30000.] ;use 0.0 for lower bound since the sc_pot is used to set this
→ Allowed energy range for moment calculations
→ Affects calculations L416-22:
JEe_Tot, JEe, Je, Je_lc

energy_ions=[0.,500.] ;use 0.0 for lower bound since the sc_pot is used to set this
→Allowed energy range for moment calculations
→ Affects calculations of both ies and TEAMS data! (L425-48):
JEi, Ji, JEi_up, Ji_up, JEp_up, JEo_up, JEh_up, Jp_up, Jo_up, Jh_up
### How mapping to ionosphere takes place
;;Scale electron energy flux to 100km, pos flux earthward
get_data,'ILAT',data=tmp
sgn_flx = tmp.y/abs(tmp.y)
get_data,'B_model',data=tmp1
get_data,'BFOOT',data=tmp2
mag1 = (tmp1.y(*,0)*tmp1.y(*,0)+tmp1.y(*,1)*tmp1.y(*,1)+tmp1.y(*,2)*tmp1.y(*,2))^0.5
mag2 = (tmp2.y(*,0)*tmp2.y(*,0)+tmp2.y(*,1)*tmp2.y(*,1)+tmp2.y(*,2)*tmp2.y(*,2))^0.5
ratio = (mag2/mag1)
### Which quantities get mapped
jee_ionos_tmp_data = sgn_flx*jee_tmp_data*ratio (L618—integration over loss cone)
jee_tot_ionos_tmp_data=sgn_flx*jee_tot_tmp_data*ratio (L621—integration over all angles)
→*A subtlety: Electron energy flux in the loss cone is simply called Jee, while electron number flux in the loss cone is called Je_lc (L416-22)
#### Quantities integrated over entire interval that get mapped
→Sup with the square root? ;;“map result to ionosphere (sqrt of B since have integrated in x)”
Total ion flow over entire interval (L657)
ji_tot(jjj)=int_tabulated(position_ji,ji_tmp_data*sqrt(ratio))

Total upflow over entire interval ('jjj' denotes top-level interval—usually one or two per orbit)
ji_up_tot(jjj)=int_tabulated(position_ji,ji_up_tmp_data*sqrt(ratio)) ;mapped to ionosphere sqrt due to integration in x (L658)
→*A subtlety: Chris only integrates over HALF the angular range to exclude ram ions, and he then multiplies the calculated flux by 2.0 to account for his halving the angular range

"total electron dflux at ionosphere from single integ."
jee_tot(jjj)=int_tabulated(position_je,jee_tmp_data*sqrt(ratio)) ;mapped to ionosphere sqrt due to integration in x (L673,1318)

Integrated downgoing electron flux over that interval at ionosphere
current_intervals(j,7)=current_intervals(j,7)*sqrt(ratio(intervalparts_electrons(0))); (L881)
→CALCULATION: This and the three following (j,[41,12,13]) are calculated by interpolating the particle data to the same resolution as the fields data, and then integrating by multiplying interpolated particle data by “speed_mag_point” and using the int_tabulated function

Integrated downgoing electron flux from total distribution over that interval at ionosphere
current_intervals(j,41)=current_intervals(j,41)*sqrt(ratio(intervalparts_electrons(0))) ; (L882)
→Calculation performed as described under 'CALCULATION'

Integrated upgoing ion flux over the interval at the ionosphere
current_intervals(j,12)=current_intervals(j,12)*sqrt(ratio(intervalparts_ions(0))); (L917)
→Calculation performed as described under 'CALCULATION'

Integrated upgoing only ion flux over the interval at the ionosphere
current_intervals(j,13)=current_intervals(j,13)*sqrt(ratio(intervalparts_ions(0))); (L918)
→Calculation performed as described under 'CALCULATION'
### How quantities attributable to AWs are distinguished from others
"total electron dflux at ionosphere from single integ.",Jee_tot(jjj)
"total electron dflux at ionosphere from total of intervals",total(current_intervals(*,7))
"total Alfven electron dflux at ionosphere",total(current_intervals(keep,7))
"total ion outflow at ionosphere from single interval",Ji_tot(jjj)
"total ion outflow at ionosphere from total of intervals",total(current_intervals(*,12))
"total Alfven ion outflow at ionosphere",total(current_intervals(keep,12))
"total upward only ion outflow at ionosphere from single integ.",Ji_up_tot(jjj)
"total upward only ion outflow at ionosphere from total of intervals",total(current_intervals(*,13))
"total Alfven upward only ion outflow at ionosphere",total(current_intervals(keep,13))

→'keep' is simply an array of indices for events that are Alfvénic
→Note: the quantities current_intervals([],[7,12,13]), are as follows:
7-Integrated downgoing electron flux over that interval at ionosphere
12-Integrated upgoing ion flux over the interval at the ionosphere
13-Integrated upgoing only ion flux over the interval at the ionosphere
→Note: The other quantities are shown in “Quantities integrated over entire interval that get mapped”, and are as follows:
Jee_tot(jjj)
Ji_tot(jjj)
Ji_up_tot(jjj)